~--==CORE==--~			~--==SOUND==--~
pin	function	assignment	pin	function	assignment
1	NRST/PA1	#RST swim breakout	1	NRST/PA1	#RST swim breakout
2	OSC_IN/PA2	quartz	2	OSC_IN/PA2	quartz
3	OSC_OUT/PA3	quartz	3	OSC_OUT/PA3	quartz
4	PA4	NC	4	PA4	NC
5	PA5	NC	5	PA5	NC
6	PA6	NC	6	PA6	NC
7	Vss	GND	7	Vss	GND
8	Vdd	+3.3V	8	Vdd	+3.3V
9	PD0	SD_Sb	9	PD0	NC
10	PD1	PD1 breakout	10	PD1	NC
11	PD2/TIM1CH1	SOUND(24): PD7 – clock distribution	11	PD2	NC
12	PD3	PD3 breakout	12	PD3	NC
13	PB0	PB0 breakout	13	PB0	NC
14	PB1	PB1 breakout	14	PB1	NC
15	PB2	PWOK input	15	PB2	NC
16	PB3	#PWON output	16	PB3	NC
17	PB4/NSS	NC	17	PB4/DAC_OUT	RC low-pass
18	PB5/SPI_SCK	SD_CLK	18	PB5	NC
19	PB6/SPI_MOSI	SD_DI	19	PB6	NC
20	PB7/SPI_MISO	SD_DO	20	PB7	NC
21	PD4	#SD_CS	21	PD4	NC
22	PD5	NC	22	PD5	NC
23	PD6	#SC16_RESET	23	PD6	NC
24	PD7	#SC16_IRQ	24	PD7	CORE(11): TIM1CH1
25	PC0/I2C_SDA	SC16_SDA	25	PC0	ENA3
26	PC1/I2C_SCL	SC16_SCL	26	PC1	NC
27	PC2	ENA2 breakout	27	PC2	NC
28	PC3	ENA3 (sound_enable)	28	PC3	NC
29	PC4	ENA1 breakout	29	PC4	NC
30	PC5/TX	TX breakout + sound_rx	30	PC5/TX	RX3
31	PC6/RX	RX1/RX2/RX3 selected by ENAx	31	PC6/RX	TX
32	SWIM	SWIM swim breakout	32	SWIM	SWIM swim breakout

~--==SC16IS741==--~			~--==74HC126==--~			~--==NE5532==--~
pin	function	assignment	pin	function	assignment	pin	function	assignment
1	Vdd	+3.3V	1	E1	NC	1	A_OUT	AOUT
2	A0	VCC	2	A1	NC	2	-A_IN	AOUT
3	A1	VCC	3	Y1	NC	3	+A_IN	RC low-pass from DAC
4	DO	NC	4	E2	ENA2, CORE(27)	4	-Vs	GND
5	SCL	SCL, CORE(26)	5	A2	RX2	5	+B_IN	AVCC
6	SDA	SDA, CORE(25)	6	Y2	RX	6	-B_IN	pin 7
7	#IRQ	CORE(24)	7	GND	GND	7	B_OUT	pin 6
8	I2C	VCC	8	Y3	RX	8	+Vs	AVCC (9V)
9	Vss	GND	9	A3	RX1
10	#RTS	NC	10	E3	ENA1, CORE(29)
11	#CTS	NC	11	Y4	RX
12	TX	TX UART breakout	12	A4	RX3, SOUND(30)
13	RX	RX UART breakout	13	E4	ENA3, CORE(28), SOUND(25)
14	#RESET	CORE(23)	14	VCC	+3.3V
15	X1	Q, 22 pF
16	X2	Q, 30 pF